## Slide 1
B+ trees

## Slide 2: Outline
Motivation:
  Hard drives accesses are slow
  Reduces the number of disk accesses
B+ trees:
  Description
  Insertion and deletions

## Slide 3: Hard Drives
Main memory is limited: MiB-GiB
Caches even more so: KiB-MiB
Hard drives, however, are rich: GiB-TiB
  The cost is speed...
  Platters spin at
  3600-7200 rpm
Hewlett-Packard http://www.hp.com/

## Slide 4: Hard Drives
Recall:
  1 kB = 1000 bytes 1 KiB = 210 bytes = 1 024 bytes
  1 MB = 106 bytes 1 MiB = 220 bytes = 1 048 576 bytes
  1 GB = 109 bytes 1 GiB = 230 bytes ≈ 1.073 · 109 bytes
  1 TB = 1012 bytes 1 TiB = 240 bytes ≈ 1.100 · 1012 bytes

## Slide 5: Hard Drives
Access time for these devices is variable:
  Cache 1 GHz
  Main memory (SDRAM): 100 MHz
  Hard drive (10 ms seek time) 100 Hz
A factor of ten million

## Slide 6: Hard Drives
Consider the one second it takes to retrieve a book from a bookshelf
In 107 s (four months):
  Walk from Waterloo to Ottawa
  Pick up a book in the National Archives, and
  Walk home with months to spare

## Slide 7: Hard Drives
No wonder Marvin the Paranoid Android is always bored when he deals with humans
  1 Hz
  10 Hz if typing
Copyright © 1982 by the B.B.C.

## Slide 8: Hard Drives
Main memory (in general) is byte addressable
  Each byte has its own address
  Each byte can be accessed or modified
To access a bit, you must access the byte containing it

## Slide 9: Hard Drives
Hard drives are block addressable
  The block size is variable
  We will assume blocks are 4 KiB
To access a byte from a block, you must load the entire block containing it

## Slide 10: Hard Drives
The I/O controller on the hard drive reads and writes to the hard drive in blocks
  The block is copied to main memory
  Direct memory access (DMA)
To access one byte on the hard drive, the controller loads the entire 4 KiB block

## Slide 11: Hard Drives
Accessing/modifying a byte in main memory:
Accessing/modifying a byte on a hard drive:
Hard drive
Main memory
Hard drive
Main memory
Main memory
Main memory

## Slide 12: Hard Drives
When you format your hard drive, you specify the block size
All files occupy an integral number of blocks
  The last block may be part empty

## Slide 13: Hard Drives
For example, the previous image of the hard drive occupies 69 714 bytes
Requires 18 4-KiB blocks 18 × 4098 bytes = 73 728 bytes

## Slide 14: Hard Drives
Consequence: 4014 bytes are unused
  Large block sizes will waste space

## Slide 15: Hard Drives
In summary:
  Hard drives are slow
  Divided into blocks
    We will use a 4 KiB block size
  Accessing the entire block costs the same as accessing one byte within the block

## Slide 16: Storing Very Large Trees
Problem:
  Suppose we are attempting to store a large amount of ordered data
  We will consider 109 items
    A 4-byte (well ordered) key and associated data
    Pointers assumed to be 4 bytes

## Slide 17: Storing Very Large Trees
Restrictions and Assumptions:
  This must be stored on a hard drive
    32 bits only access 4 GiB
    Main memory is volatile
  Assume the root node is in main memory
  Block addresses are 32 bits
  Processor speed: 3 GHz
  Hard drive seek time: 10 ms

## Slide 18: Storing Very Large Trees
We have assumed that all balanced trees are comparable: Q(ln(n))
  This will not always apply
Consider
  Binary search trees
  M-way trees
  Realistic M-way trees
  B+ trees

## Slide 19: Binary Search Trees
A binary search tree with 109 entries has a minimum height of ⌊lg(109)⌋ = 29
Just the pointers requires almost 8 GiB
  32 bits can access at most 4 GiB of main memory

## Slide 20: Binary Search Trees
It is very likely that two nodes are not in the same block on the hard drive
  Accessing leaf node requires that 29 blocks be copied from the hard drive
  Assume the root is in main memory
With 10 ms seek time, this would require approximately 0.29 s

## Slide 21: M-Way Search Trees
Let us try to fit as many keys and pointers into one block
  Keys are 4 bytes
  Assume pointers are 32 bits (4 bytes)
A block is 4 KiB:
  4 KiB / (4 bytes + 4 bytes) = 512
Store a 512-way node in each block

## Slide 22: M-Way Search Trees
An optimal 512-way tree would be of height ⌊log512(109)⌋ = 3
Searches requires at most 30 ms
  Almost 10 times faster than a binary search tree

## Slide 23: M-Way Search Trees
Problem:
  We are only storing keys and pointers
That’s like storing
  UW Student IDs
  Bank account numbers
but no information
In general, we want to store more information...

## Slide 24: M-Way Search Trees
Assume we wish to store:
  a 4 byte key
  a 4 byte pointer (to a child block), and
  100 bytes of information
Consequently
Each block can store 37 records
  Use a 38-way tree

## Slide 25: M-Way Search Trees
A 4 KiB block would be partitioned as follows:
  37 records with keys
  38 next pointers
  96 bytes left over
4096 B

## Slide 26: M-Way Search Trees
Hence, the maximum height would be
⌊log38(109)⌋ = 5
This would increase search time by 67% over a 512-way tree

## Slide 27: M-Way Search Trees
Problem:
  We don’t want to increase the run-time
  Recall that 31/32 ≈ 97% of all records are already in the leaves
Solution:
  Move all data (4-byte key and100 bytes per record) into the leaves

## Slide 28: M-Way Search Trees
Consider this 3-way tree
  Integer keys and data

## Slide 29: M-Way Search Trees
Move all data to the leaves
  We must still know which leaf to access

## Slide 30: M-Way Search Trees
For example, we could store the minimum and maximum values in each tree
  Expensive...

## Slide 31: M-Way Search Trees
Instead, recall that our goal is to make each node (leaf or internal) fit into one block (e.g., 4 KiB)
  If we are not storing data, we can store more keys and pointers
  Let the internal nodes be M-way trees where

## Slide 32: M-Way Search Trees
We could use a 5-way tree
  Store the smallest entries of all but the first sub-tree

## Slide 33: M-Way Search Trees
We can do this at all levels

## Slide 34: M-Way Search Trees
Searching is now straight-forward:
  Find entries 28 and 63

## Slide 35: B+ Trees
A B+ tree uses this idea
  Adds restrictions to ensure balance and consistency
The goal is to:
  Minimize disk accesses
  Fix access time
Data is stored in leaf nodes and internal nodes are M-way trees

## Slide 36: B+ Trees
The block size will affect:
  The amount of data stored in leaf blocks
  The choice of M for the internal blocks
Maximize the amount of data which can be stored in one 4 KiB block

## Slide 37: B+ Trees
Suppose our key is 4 bytes and we are storing 100 bytes per record
Thus, our leaf blocks will store 39 records with 40 bytes left over
4096 B

## Slide 38: B+ Trees
Next, we must represent store the internal blocks
Because all information is in the leaf blocks, we only need to store:
  Keys (to allow navigation) and
  Pointers

## Slide 39: B+ Trees
Thus, within a 4 KiB block, we could store 512 key-address pairs
This allows us to use a 512-way tree
  The 4 bytes left over could store the number of entries
  Not all internal blocks will be full
4096 B

## Slide 40: B+ Trees
One billion records requires
  109/39 = 25 641 026 leaf blocks
  A 512-way tree of height h can store 512h + 1 entries in the deepest nodes
Including the links to the leaf nodes, the tree height is h = 3

## Slide 41: B+ Trees
Any search would require three disk accesses, or 30 ms
  The root is always in memory
  We search for the required child

## Slide 42: B+ Trees
Loading the child requires 10 ms
  A search indicates which child to access

## Slide 43: B+ Trees
The 2nd level requires another 10 ms to load
  A search indicates which leaf block to load

## Slide 44: B+ Trees
Finally we load the leaf block: 10 ms
  Search the 39 records for the one of interest

## Slide 45: B+ Trees
A B+ tree is a tree where
  All the leaf blocks are arrays with L records sorted on a key
  All internal blocks are M-way trees with M – 1 keys and M sub-trees

## Slide 46: B+ Trees
This defines the general shape of a B+ Tree
We will require that all leaf blocks are at the same height
  Guarantees the same access time for all records

## Slide 47: B+ Trees
A B+ trees of height 1 and 2 with
  32-way internal blocks M = 32
  8 records per leaf blocks L = 8
32-way trees
leaf blocks: L = 8

## Slide 48: B+ Trees
These images show perfect B+ trees
  Best possible case
256 records
8192 records

## Slide 49: B+ Trees
In most cases the nodes will not be full
  Partially filled leaf blocks
  Internal nodes with less than M sub-trees
A few additional rules ensure a reasonable balance

## Slide 50: B+ Trees
Define a B+ tree of order M as follows:
  All data is stored at the leaf blocks
  If there are no more than L entries, the root node is a leaf block
  Otherwise, all leaf blocks are
    At the same depth
    Contain between ⌈L/2⌉ and L entries
      At least half full
    L depends on the size of the records being stored and the size of the blocks

## Slide 51: B+ Trees
  The root nodes is either:
    A leaf block, or
    An M-way tree with between 2 and M children
  All other internal blocks are M-way trees with ⌈M/2⌉ to M children
    The internal blocks store up to M – 1 keys to guide the searching where key k represents the smallest key in sub-tree k

## Slide 52: B+ Trees
The best case height for our example was:
Assuming the worst case
  All child blocks are half filled (20), and
  All internal nodes are half filled (256)
then the height of the tree is

## Slide 53: B+ Trees
If we wanted to store 10 trillion entries with M = 512, L = 39
  Best case:
  Worst case:

## Slide 54: B+ Trees
Recall that the our block size is fixed at 4 KiB
  Consequently, we may consider any operations that manipulate these blocks to be Q(1)
  Technically the array manipulations are O(L) and O(M), but both L and M depend entirely on the block size
  Thus, all operations will have the same run-time Q(ln(n))
    Note that unlike AVL trees, we must always access a leaf node

## Slide 55: Example
Consider the following B+ tree
  M = 5, L = 3 and 54 records

## Slide 56: Example
The root node guides the search for keys:
  The 1st subtree contains all objects x < 21
  The 2nd, all objects 21 ≤ x < 49
  The 3rd, all objects 49 ≤ x < 67 and
  The 4th, all objects x ≥ 67

## Slide 57: Find
Searching for 14:
  14 < 21 check 1st subtree
  12 ≤ 14 < 18 check 3rd leaf block

## Slide 58: Find
Searching for 65:
  49 ≤ 65 < 67 check 3rd subtree
  63 ≤ 65 check 4th leaf block

## Slide 59: Find
Searching for 71:
  67 ≤ 71 check 4th subtree
  71 < 74 check 1st leaf block

## Slide 60: Find
The root node is always in main memory
Each find required that 2 blocks be loaded into main memory
  Total time: 20 ms
If the associated record is modified, the leaf block must be saved
  Total time: 30 ms

## Slide 61: Insert
Suppose we insert a new record into the B+ tree
  Follow the same search pattern as find
  If the record is not in the corresponding leaf block, add it and save the block
  If the leaf block is full, split it into two leaf blocks with the records split between the two nodes
    Each leaf block is guaranteed to be at least half full
  It is necessary to update the parent

## Slide 62: Insert
Suppose we insert 55
  49 ≤ 55 < 67 check 3rd subtree
  54 ≤ 55 < 58 check 2nd leaf block

## Slide 63: Insert
55 is not in this leaf block and the block is not full
  We add it by doing an O(L) insertion into the array

## Slide 64: Insert
The modified leaf block must now be saved to the hard drive

## Slide 65: Insert
Next, insert 87
  67 ≤ 87 check 4th subtree
  85 ≤ 87 < 91 check 4th leaf block

## Slide 66: Insert
Again, the leaf block is not full, so we add it

## Slide 67: Insert
As long as the corresponding leaf node is not full, insertion is similar to a find followed by a write
  The insertion itself may be O(L), but this is trivial relative to the time required to perform even one write to the disk
Total time: 20 ms + 10 ms = 30 ms

## Slide 68: Insert
Consider inserting 60

## Slide 69: Insert
Consider inserting 60

## Slide 70: Insert
Both immediate siblings are full
  Split the leaf block into two, each of which are at least half full

## Slide 71: Insert
The parent must be modified to account for this new node:
  Add 60 to the parent and update the pointers

## Slide 72: Insert
Consider inserting 11

## Slide 73: Insert
Both siblings are full, so split the leaf block

## Slide 74: Insert
The parent must be updated to accommodate the new leaf block

## Slide 75: Insert
In addition to loading the two blocks, it is now necessary to:
    Save the modified leaf block,
    Save the new leaf block, and
    Save the parent.
Total time: 20 ms + 30 ms = 50 ms
Problem: what happens if the parent is full, too?
  We must recurse back to the root

## Slide 76: Insert
Consider inserting 35

## Slide 77: Insert
The leaf block is full, so we split it
  The parent block, however, is also full

## Slide 78: Insert
We can split the parent block in two

## Slide 79: Insert
At this point, the root node must also be updated

## Slide 80: Insert
In addition to loading the two blocks, it is now necessary to:
    Save the new and the modified leaf blocks,
    Save the new and modified internal blocks, and
    Save the root.
Total time: 20 ms + 50 ms = 70 ms
Problem: what happens if the parent is full, too?
  We must recurse back to the root

## Slide 81: Insert
Once again, the root node is updated allow a successful search for any key

## Slide 82: Insert
Consider inserting 86

## Slide 83: Insert
Again, the leaf block is full, so we must split it

## Slide 84: Insert
However, the parent node is also full

## Slide 85: Insert
We must split the parent block as well, but the root node is also full
  Split the root node into two nodes

## Slide 86: Insert
This, however, is no longer a tree:
  In order to create a tree, we must introduce a new root node

## Slide 87: Insert
The root node is only required to have at least two children
  We store the smallest entry in the newly created 2nd tree: 49

## Slide 88: Insert
Everything in the first subtree of the root is less than 49
Everything in the second subtree is greater than or equal to 49

## Slide 89: Insert
In addition to loading the two blocks (20 ms), it is now necessary to:
    Save the new and the modified leaf blocks,
    Save the new and modified internal blocks,
    Save the previous root and its new sibling, and
    Save the new root node.
Total time: 20 ms + 70 ms = 90 ms

## Slide 90: Insert
We can only grow the height of the tree by adding a new root
  Thus, all children are now at depth 3

## Slide 91: Insert
At this point, the leaves are more sparse as are most internal nodes
  10, 19, 34, 37, 38, 62, 89 and 90 could be added to existing leaf blocks
  22, 23, 29, 31, 41, 44, 46, 47, 68, 70, 72, 73, 76, 77, 80, 83, 84, 93, … could be added requiring that only the parent be modified

## Slide 92: Insert
For example, consider adding 70

## Slide 93: Insert
This only requires that leaf block to be split its parent to be updated

## Slide 94: Insert
The addition 0, 1, 13, 16, 17, 50, 57or 65 would still result in the parent being split

## Slide 95: Insert
However, adding 65 fills the corresponding leaf block

## Slide 96: Insert
This would again update the parent

## Slide 97: Insert
Inserting 77 would split the leaf block, but only update the parent

## Slide 98: Insert
Finally, we could insert 80 to split that leaf block and its parent

## Slide 99: Insert
The leaf is full, but so is its parent

## Slide 100: Insert
Again, we would have to split the parent node and update its parent

## Slide 101: Insert
At this point, it would seem that such splits occur very often
In reality, recall that with values such as M = 512 and L = 32:
  A split of a leaf node would occur, on average, once every 16 insertions
  A split of a parent would occur once every 256 splits of a leaf
These are reasonably rare events

## Slide 102: Erase
When erasing a record from a B+ tree, it may occur that an insertion will result in a violation in a leaf node:
  It end up with < L/2 entries
It would be necessary to either merge or redistribute records between the leaf blocks
  Two leaf blocks may have ≤ L records: merge them
  Otherwise, they may have > L nodes: redistribute

## Slide 103: Erase
Similarly, an internal node may end up with fewer than M/2 children
Ultimately, a root node with two children may see those children merged
  This is solved by removing the old root node and defining the newly merged node to be the new root

## Slide 104: Erase
Similarly, an internal node may end up with fewer than M/2 children
Ultimately, a root node with two children may see those children merged
  This is solved by removing the old root node and defining the newly merged node to be the new root

## Slide 105: Erase
To allow easier erasing of records, one other feature is standard with a B+ tree:
  The leaf blocks are usually linked in order forming either a singly or doubly linked list
This allows fast access to either the preceding or succeeding child block:
  If an erase reduces a leaf block to less than half full, check the neighbouring siblings

## Slide 106: Erase
Let’s start with the B+ tree in the following state:

## Slide 107: Erase
Erasing 98 (and any associated record) is straight-forward
  Remove the record and save the leaf block

## Slide 108: Erase
The leaf block is still at least half full

## Slide 109: Erase
Removing 75 requires us to move the records in that leaf block up

## Slide 110: Erase
The leaf block must now be saved

## Slide 111: Erase
If we remove record 39, we need to update the leaf block

## Slide 112: Erase
But we must also update the parent
  A re-insertion of 39 will put it into the leaf block containing 35

## Slide 113: Erase
Remove 59 gives us two choices

## Slide 114: Erase
We could access the left sibling and copy over 56
  Redistribution

## Slide 115: Erase
Alternatively, we could merge that leaf block with the right sibling

## Slide 116: Erase
At this point, the parent node must also be updated

## Slide 117: Example: Removal
Erasing 35 would result in another leaf block less than half full
  We will merge it with its right sibling—easier to deal with as they share a common parent

## Slide 118: Erase
The parent, however, is now less than half full

## Slide 119: Erase
It might be possible to copy over one leaf block from the next internal node
  Redistribution

## Slide 120: Erase
The other solution, more reasonable as they share a common parent, is to merge the two internal nodes

## Slide 121: Erase
As before, however, that node is now less than half full
  Merge it with its sibling

## Slide 122: Erase
There is no longer a purpose to the root node:
  Delete the old root and assign the one child to be the new root

## Slide 123: Erase
The result is a B+ tree with one lower height

## Slide 124: Erase
Erasing 88 now reduces that leaf block to less than half full: merge

## Slide 125: Erase
The parent, too, is now half full: merge

## Slide 126: Erase
The final result is a well defined B+ tree

## Slide 127: Terminology
The original B tree had records stored at each node:
  An M-way tree with all leaf blocks at the same depth and no node (other than the root) half full
  Developed by Rudolf Bayer and Edward M. McCreight in 1972
  The “B” is for balanced
2-3 trees are B-trees with M = L = 3
2-3-4 trees are B-trees with M = L = 4
  Available at http://ece.uwaterloo.ca/~dwharder/aads/Algorithms/
The B+ tree was already in use by 1973

## Slide 128: B* Trees
We require that all blocks be half full
Must we be this sparse?
  Is there a larger lower bound we can use?
We can require that nodes be 2/3 full
  Called a B*-tree
  Insertions result in redistributions between both left and right siblings
    If both siblings are full, the node and one sibling are split into three, each of which will be 2/3rds full
  Erases result in more redistributions
    If both siblings are 2/3rds full, merge them into two full nodes

## Slide 129: B+ trees
In this topic, we have covered B+ trees:
  Used for storing large amounts (GiB) of information
  Internal nodes are M-way trees storing pointers with keys
  Leaf blocks contain L records with keys
  All nodes (except the root) must always be at least half full
  Splitting nodes is used for insertions
  Redistributions and merging are used for erases
  B* trees have less wasted space

## Slide 130: References
[1] Cormen, Leiserson, and Rivest, Introduction to Algorithms, McGraw Hill, 1990, Ch. 19, p.381-99.
[2] Weiss, Data Structures and Algorithm Analysis in C++, 3rd Ed., Addison Wesley, §4.7, p.159-64.

## Slide 131: References
Wikipedia, http://en.wikipedia.org/wiki/B+_tree
[1] Cormen, Leiserson, and Rivest, Introduction to Algorithms, McGraw Hill, 1990, Ch. 19, p.381-99.
[2] Weiss, Data Structures and Algorithm Analysis in C++, 3rd Ed., Addison Wesley, §4.7, p.159-64.
These slides are provided for the ECE 250 Algorithms and Data Structures course. The material in it reflects Douglas W. Harder’s best judgment in light of the information available to him at the time of preparation. Any reliance on these course slides by any party for any other purpose are the responsibility of such parties. Douglas W. Harder accepts no responsibility for damages, if any, suffered by any party as a result of decisions made or actions based on these course slides for any other purpose than that for which it was intended.