## Slide 1: Course introduction

## Slide 2: Introduction
In this topic, we will
  Give motivation for this course
  Describe the difference between discrete mathematics and calculus (continuous mathematics)
  Look at issues of trying to use computers to solve problems in calculus
  Describe absolute and relative error
  Describe the decimal and binary representation of real numbers
  Define rounding and significant digits
  Describe the difference between accuracy and precision
  Given an overview of the balance of this course

## Slide 3: Background
Engineering design involves the application of mathematics and science to solve real-world problems
  A failure of a design may cause harm to life, health, the environment or the finances of a client or the public
The real world is modeled through equations and differential equations
  Conservation and other physical laws
  Relationship between forces
  The superposition principle

## Slide 4: Background
Only the most trivial problems can be solved exactly
  If a problem can be solved exactly, what is the need for an engineer?
Problems can almost always be solved using a myriad of different approaches
  Seldom, if ever, is there only one ideal approach
  Each approach will have benefits and drawbacks that must be quantified and analyzed

## Slide 5: Background
In determining the most appropriate approach, it is necessary to test the various solutions
  For example,
    How robust is a solution
    Is the solution sensitive to initial conditions?

## Slide 6: Background
One possible solution:
  Build multiple instances of your design and test them
  This is exceptionally costly
Alternatively, if we have a mathematical description, can we not implement and simulate it, instead?

## Slide 7: Background
For example, a circuit is described by Maxwell’s equations
  This involves partial differential equations
  Using wires, this effectively restricts these equations to one dimension
  These partial differential equations can thus be simplified to differential equations
  The use of linear circuit elements such as capacitors, resistors, inductors and memristors together with alternating current can further simplify the solutions to these differential equations to algebraic equations
  Transistors, as well, may also be described linearly under the conditions of small-signal model
  More complex models may still be simulated using differential equations

## Slide 8: Background
For example, a circuit is described by Maxwell’s equations
  This involves partial differential equations
  Using wires, this effectively restricts these equations to one dimension
  These partial differential equations can thus be simplified to differential equations
  The use of linear circuit elements such as capacitors, resistors, inductors and memristors together with alternating current can further simplify the solutions to these differential equations to algebraic equations
  Transistors, as well, may also be described linearly under the conditions of small-signal model
  More complex models may still be simulated using differential equations

## Slide 9: Background
For example, consider this RLC circuit:
i1
i2
V(t)
R1
R2
C
L
+
–

## Slide 10: Background
The response of a digital circuit can be described by a system of linear equations
  This can involve millions of linear equations in an equal number of unknowns
  Solving such a system cannot be done analytically in either a reasonable amount of time or memory
Consequently, we will approximate such systems to find approximate solutions
  Such solutions use numerical algorithms

## Slide 11: Discrete mathematics and calculus
In your courses on discrete mathematics and logic, you were introduced to
  Boolean logic
  Set theory
  Combinatorics
  Graph theory
In your courses on continuous mathematics (calculus), you were introduced to
  Differentiation
  Integration
  Measure
  Infinite series

## Slide 12: Discrete mathematics and calculus
Concepts in discrete mathematics can be modeled using integers
  Large discrete systems will sometimes be approximated using continuous systems
    For example, statistics
Concepts in calculus use real numbers
  Real numbers can only be stored as approximations
  Computers use floating-point numbers
  Every floating-point number represents a rational number
    We approximate all possible real numbers using a finite number of rational approximations

## Slide 13: Approximating the derivative
For example, from calculus, we know that
Let’s try this out in C++:
    double diff( double f( double ), double x, double h ) {
    return (f( x + h ) - f( x ))/h;
    }
This can be called with
    std::cout << diff( std::sin, 1.0, 0.001 ) << std::endl;

## Slide 14: Approximating the derivative
Trying a few examples:
    Enter a value of x: 1.0
    The derivative of sine at x = 1 is 0.5403023058681398
    Enter a value of h (0.0 to quit): 0.1
    The derivative is approximately 0.4973637525353891
    Enter a value of h (0.0 to quit): 1e-5
    The derivative is approximately 0.5402980985058647
    Enter a value of h (0.0 to quit): 1e-10
    The derivative is approximately 0.5403022473871033
    Enter a value of h (0.0 to quit): 1e-15
    The derivative is approximately 0.5551115123125783
    Enter a value of h (0.0 to quit): 1e-16
    The derivative is approximately 0
    Enter a value of h (0.0 to quit): 0.0

## Slide 15: Approximating the derivative
Obviously, we have an issue here…
  The first step is to be able to describe how good an approximation is to the exact solution
  In the next topic, we will focus on the design of floating-point numbers
  The balance of the course will be focused on finding algorithms that avoid the issues with floating-point numbers

## Slide 16: Error, absolute error and relative error
If xapprox is an approximation of a value x, we write and
Consequently, the error e is always:
Usually, however, we may refer to the absolute error:
We may also refer to the relative error and percent relative error:

## Slide 17: Error, absolute error and relative error
For example, from calculus,
An approximation of f (x + h) is
The error of the approximation is
The absolute error is

## Slide 18: Error, absolute error and relative error
For example, from calculus,
The relative error, assuming f (x + h) ≠ 0, is

## Slide 19: Approximations of p
  3.14 0.001593 0.0005070 0.05 %
  22/7 0.001264 0.0004025 0.04 %
  355/113 0.0000002668 0.00000008491 0.000008491 %
Approximation | Absolute error | Relative error | Percent relative error
Note, we will always describe the absolute and relative error to four digits.

## Slide 20: Which do we prefer?
It is easier to discuss absolute error over error
  Neither, however, are unit-free:
    If you were told that the absolute error was 10 m
      This is great if you’re measuring the distance to the Moon
      Somewhat sub-optimal if you’re measuring the width of a wire
  The relative error is unit-free:
    A relative error of 0.01 means that the approximation is good to one part in a hundred, regardless of the magnitude of the exact value
    A relative error of 0.01 is a 1% relative error
  The relative error is not defined for approximating zero, but if you’re approximating zero and you know it…
Note that the Taylor series gives an absolute error

## Slide 21: Decimal and binary representations
Having described error, we will now look at the representation of real numbers:
  The decimal representation
  Binary representation
  Rounding and significant digits
TO BE RECORDED!!!!!!

## Slide 22: Decimal numbers
A non-zero real number is written as a decimal number when it is in the form
Here we have
  d0 is a non-zero digit
  Each other dk is a decimal digit
  The exponent e is an integer
This is usually contrasted with fractional form for rational numbers

## Slide 23: Decimal numbers
If e is small in magnitude, we may simply move the decimal point:
For example,

## Slide 24: Decimal numbers
If dk = 0 for all k > n, we will say
has a terminating decimal representation

## Slide 25: Decimal numbers
If dk = 0 for all k > n, we will say
represents an n + 1 digit decimal number
For example,
3.140 is a 4-digit decimal number
6.62607015 × 10−34 is a 9-digit decimal number

## Slide 26: Binary numbers
A non-zero number is written as a binary number when it is in the form
Here
  The one leading bit must be non-zero; that is, 1
  Each bk in the mantissa is a binary digit or “bit”
  The exponent e is an integer
The base and exponent is usually still written in decimal

## Slide 27: Binary numbers
If e is small in magnitude, we may simply move the radix point:
For example,
We will add a subscript “2” to show a number is in binary
2
2
We can also use 0b1001101 and 0b0.0110011

## Slide 28: Binary numbers
If bk = 0 for all k > n, we will say
has a terminating binary representation

## Slide 29: Binary numbers
If bk = 0 for all k > n, we will say
represents an n + 1 bit binary number
For example,
1.010 is a 4-bit binary number
1.00111101001000 × 2−34 is a 15-bit binary number

## Slide 30: Rounding
Most real numbers have infinitely many digits
  These require an infinite number of digits to store
  Even most terminating decimal representations have far more digits than we care about
  3.1415926535897932384626433832795028841971693993751
  However, we cannot store an infinite number of digits
  In fact, the most efficient means of implementing such numbers is with a fixed number of digits
We will need to represent all such numbers by a decimal or binary number with a fixed n digits in the mantissa

## Slide 31: Rounding
Which n + 1 digit number (n digits in the mantissa) do we use to approximate any real number?
  The n + 1 digit number that has the smallest absolute error
  We will say that we round a real number x to the closest n + 1 digit decimal or binary number

## Slide 32: Rounding
Rules for decimal rounding:
  To round a decimal representation to n + 1 digits:
    If the digit dn+1 is 0, 1, 2, 3 or 4, just drop all subsequent digits
    If the digit dn+1 is 5, 6, 7, 8 or 9, but not exactly 5000···, we will
      Drop all subsequent digits
      Add “1” to dn, possibly resulting in a carry
For example,
1.534982 rounded to three digits is 1.53
1.534982 rounded to four digits is 1.535
1.534982 rounded to five digits is 1.5350
1.534982 rounded to six digits is 1.53498

## Slide 33: Rounding
Rules for binary rounding:
  To round a binary representation to n + 1 bits:
    If the next bit bn+1 = 0, just drop all subsequent bits
    If the next bit bn+1 = 1 but not exactly 1000···, we will
      Drop all subsequent bits
      Add “1” to the last bit bn, possibly resulting in a carry
For example,
1.1011011 rounded to three bits is 1.11
1.1011011 rounded to four bits is 1.110
1.1011011 rounded to five bits is 1.1011
1.1011011 rounded to six bits is 1.10111

## Slide 34: Rounding
We skipped two cases:
Both these numbers are half-way between two n + 1 digit numbers
  Do we round down (truncate) or round up (truncate and add)?
  If we choose one of these options, we will introduce a bias into calculations
  Thus we choose one 50% of the time, and the other the other 50% of the time:
    If dn is odd, we increment it, otherwise we leave it
    If bn = 1, we increment it, otherwise we leave it

## Slide 35: Rounding
Note that we have only discussed rounding in our formal representation
If the decimal/radix point is anywhere else, we count the digits starting at the most significant digit:
  0.0005838125 rounded to 4 digits is 0.0005838
  108513.829 rounded to 3 digits is 109000,
  but it’s clearer if we present it as 1.09 × 105
  0.000110001012 rounded to 5 bits is 0.000110012
  111001010.0012 rounded to 4 bits is 1110000002,
  but it’s clearer if we present it as 1.110 × 28

## Slide 36: Significant digits
Another colloquial means of describing the relative error is to use the concept of significant digits
  We will never calculate this explicitly
    Instead, we will use the number of significant digits to give a rough estimate of the relative error
      1 significant digit is a relative error no greater than 50%
      2 significant digits is a relative error no greater than 5%
  A rough approximation is as follows:
    xapprox approximates x to d significant digits if both x and xapprox rounded to d digits agree in all digits

## Slide 37: Significant digits
From the definition, we can find a formula to calculate the number of significant digits given the relative error:

## Slide 38: Approximating the square root of two
The ancient Babylonians were aware that:
  Thus, if x approximates , it follows the average of x and 2/x must be a better approximation

## Slide 39: Approximating the square root of two
  1 0.4142 0.2929 29.29 % 1
  1.5 0.08579 0.06066 6.066 % 1
  1.416666666 0.002453 0.001735 0.1735 % 3
  1.414215686 0.000002124 0.000001502 0.0001502 % 6
Approximation | Absolute error | Relative error | Percent relative error | Significant digits
Note, we will always round the absolute and relative error to four digits.

## Slide 40: Precision versus accuracy
The concepts of precision and accuracy are usually introduced via references to firearms
  The Tikka t3x tact a1 is a more precise firearm than the AK-47

## Slide 41: Precision versus accuracy
Suppose we take these firearms to the range
  The Tikka t3x tact a1 is a more precise firearm than the AK-47
  Give each rifle to a novice, the precision will be reduced:
  Introduce an error into the sights reduces the accuracy

## Slide 42: Precision versus accuracy
“Precision” refers to the degree of consistency or repeatability in measurements or system outputs, indicating how closely repeated measurements or operations agree with each other
  A ruler is less precise than a micrometer
“Accuracy” refers to the degree to which a measurement or system output matches the true or accepted value of the quantity being measured.

## Slide 43: Precision versus accuracy
Suppose you have a sensor reading an analog signal
  These readings are from a sensor that is reasonably precise and the readings are accurate

## Slide 44: Precision versus accuracy
Suppose you have a sensor reading an analog signal
  If the sensor is not correctly calibrated, the sensor is still precise, but the readings are no longer accurate

## Slide 45: Precision versus accuracy
Suppose you have a sensor reading an analog signal
  You can spend less money and purchase a less precise sensor
  These readings are still as accurate as you can expect…

## Slide 46: Precision versus accuracy
Suppose you have a sensor reading an analog signal
  Again, a less-precise sensor can also be poorly calibrated, resulting in less accurate readings than may be possible

## Slide 47: Precision versus accuracy
Suppose you have a sensor reading an analog signal
  A precise sessor with accurate readings may be made less accurate if the sensor is subject to an electric or mechanical shock

## Slide 48: Precision versus accuracy
Suppose you have a sensor reading an analog signal
  A sensor can lose precision over time if it is not maintained

## Slide 49: Precision versus accuracy
Suppose you have a sensor reading an analog signal
  Another loss in accuracy may result from a drift in settings

## Slide 50: Precision versus accuracy
When solving a problem numerically, we will use one or more different algorithms
We will describe an algorithm through its accuracy and its precision
  In general, all of our algorithms are parameterized by at least one value:
    A value of h that may be made arbitrarily small
    An integer n that may be made arbitrarily large
  In approximating a solution x,
    An algorithm is accurate if as our parameters are adjusted, the absolute error is correspondingly reduced
    One algorithm is more precise than another if the absolute error for the first algorithm is generally less than the absolute error of another

## Slide 51: Precision versus accuracy
Suppose you want to calibrate an analog-to-digital converter (adc), we require the maximum range of voltages [a, b]
What is a good approximation of a?
  How about min{x1, x2, x3, x4} ?
  You can show that this is a good approximation of not a but
  Similarly, max{x1, x2, x3, x4} is a good approximation of
  This gives us two equations:

## Slide 52: Precision versus accuracy
This gives us a system of two linear equations in two unknowns:
Using linear algebra, we may now solve for both a and b:

## Slide 53: Precision versus accuracy
Consequently,
is a less accurate approximation of a than
The mathematics is beyond the scope of this course, but the first is more precise than the second
  It has a smaller standard deviation

## Slide 54: Precision versus accuracy
Suppose we are uniformly sampling from the interval [5, 25]
We could take 10 readings:
8, 18, 16.8, 18.8, 13.4, 13 21, 15, 18, 9.6
  We see the minimum of these, 8, is an okay approximation to 5
We could take 20 readings:
14.2, 16.4, 5.6, 10.8, 9.4, 24.8, 19.6, 13.8, 5.4, 14.6, 22.6, 24.6, 12.6, 8.4, 14.2, 8.8, 11.8, 23.6, 22.6, 14.2
  We see the minimum of these, 5.4, is a more accurate approximation of 5
As n becomes larger, it seems that the minimum is a better approximation of the lower bound 5

## Slide 55: Precision versus accuracy
If we modify the other formula for more samples, we:
For the previous examples, we have

## Slide 56: Looking ahead
Thus, given n samples from [a, b]
  The minimum of the n samples is not as accurate as our linear combination of the minimum and maximum
  The minimum of the n samples is more precise than our linear combination of the minimum and maximum
  As we increase n, both formulas become more precise and accurate

## Slide 57: In this courses…
The next topic in this course is to look at floating-point numbers
  Floating-point numbers only approximate real numbers
  There will be issues with them
    Recall that we could not even precisely approximate the derivative using them
The balance of this course will be looking at numerical algorithms in order to:
  Approximating the value of an expression
  Approximating solutions to algebraic equations and systems
  Approximating solutions to analytic equations and systems
  Optimization

## Slide 58: Summary
Following this topic, you now
  Understand the purpose of this course
  Are aware of the differences between discrete mathematics and continuous mathematics (calculus)
  Have observed that floating-point numbers cause issues
  Know the ideas behind:
    Absolute and relative errors
    Decimal and binary representations of numbers
    Rounding and significant digits
  Understand the concepts of accuracy and precision
  Have an overview of what will be covered in the upcoming lectures

## Slide 59: References
[1] https://en.wikipedia.org/wiki/Rounding
[2] https://en.wikipedia.org/wiki/Accuracy_and_precision
[3] https://en.wikipedia.org/wiki/Significant_figures
[4] https://en.wikipedia.org/wiki/Approximation_error

## Slide 60: Acknowledgments
Anurag Devadiga for many excellent suggestions and comments.

## Slide 61: Colophon
These slides were prepared using the Cambria typeface. Mathematical equations use Times New Roman, and source code is presented using Consolas. Mathematical equations are prepared in MathType by Design Science, Inc.
Examples may be formulated and checked using Maple by Maplesoft, Inc.
The photographs of flowers and a monarch butter appearing on the title slide and accenting the top of each other slide were taken at the Royal Botanical Gardens in October of 2017 by Douglas Wilhelm Harder. Please see
https://www.rbg.ca/
for more information.

## Slide 62: Disclaimer
These slides are provided for the ece 204 Numerical methods course taught at the University of Waterloo. The material in it reflects the author’s best judgment in light of the information available to them at the time of preparation. Any reliance on these course slides by any party for any other purpose are the responsibility of such parties. The authors accept no responsibility for damages, if any, suffered by any party as a result of decisions made or actions based on these course slides for any other purpose than that for which it was intended.