## Slide 1: Approximating solutions to the heat equation

## Slide 2: Introduction
In this topic, we will
  Introduce the heat equation
  Convert the heat equation to a finite-difference equation
  Discuss both initial and boundary conditions for such a situation in one dimension
  Look at an implementation in Matlab
  Look at two examples
  Discuss Neumann conditions and look at the necessary modifications required and additional examples

## Slide 3: Partial differential equations
The heat equation models the transfer of heat within a system
  The value a is the diffusivity coefficient, which is proportional to how quickly heat can travel throughout the medium
If the heat transfer is restricted to one dimension, this simplifies to
  This is the case if it is heat transfer along a wire

## Slide 4: Partial differential equations
In one dimension, this says:
  The rate of change of the temperature over time is proportional to the concavity of the temperature in space
  If the concavity is locally zero (the temperature is constant or linearly changing), there is no local change in temperature

## Slide 5: Partial differential equations
In one dimension, we can substitute our two approximations:
  Note we are only using the O(h) approximation
We can rewrite this as follows:
  Compare this with Euler’s method:

## Slide 6: Partial derivatives
Suppose we have a wire or other connection between two large bodies:
  For example, with Dirichlet conditions, one end may be in contact with a body that is 100°C while the other may be in contact with a cooling unit at 0°C
  When the system is turned on, the wire has a temperature at each point
    Perhaps 20°C
  After a few seconds, depending on the material, the temperature near the heat source will increase, while the temperature near the heat sink will decrease, though more slowly

## Slide 7: Approximating partial derivatives
Suppose here we have our system:

## Slide 8: Approximating partial derivatives
Thus, represent the temperature of the bar by a function
u(x, t)
  The spatial variable x must fall between the two end-points:
  a ≤ x ≤ b
  Suppose the end points are [0, 1], in which case u(0.5, t) is the temperature at the mid-point at time t
    If t = 0 s, then the temperature is the initial temperature 20°C
    Suppose t = 10 s
      If the material is insulating (e.g., wood), it is unlikely the temperature will be very different
      If the material conducts heat rapidly (aluminium), it may already be getting warm to the touch
    After a long time, we expect the temperature in the middle to be the average of the boundary values 50°C

## Slide 9: Functions of a vector variable
We don’t know what u(x, t) is, so we will approximate it
  First, divide the interval [a, b] into nx sub-intervals, each of width h
  Thus, xk = a + kh so and
Next, we cannot approximate the solution at each point in time, so we will break time into steps
  Define tℓ = t0 + ℓDt
We will try to approximate u(xk, tℓ)
  As before, u(xk, tℓ) ≈ uk,ℓ

## Slide 10: Functions of a vector variable
To start, we have our initial conditions:
  In this case, u(xk, t0) ≈ uk,0= 20°C for an k = 1, 2, …, nx – 1
We also have two boundary conditions:
  One side of the bar is in contact with a heat sink at 0°C
    Thus, u(a, tℓ) = u(x0, tℓ) = u0, ℓ = 0 for ℓ = 0, 1, 2, 3, …
  The other side is in contact with a heat source at 100°C
    Thus, u(b, tℓ) = = 100 for ℓ = 0, 1, 2, 3, …
ℓ
k
uk,ℓ
0
1
2
3
4
5
6
7
8
9
10
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14

## Slide 11: Functions of a vector variable
So now what?

## Slide 12: Functions of a vector variable
Let’s zoom in:
ℓ
k
uk,ℓ
0
1
2
3
4
5
6
7
8
9
10
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14
ℓ
k
0 1 2 3 4
10
9
8
7
u10,0
u9,0
u8,0
u7,0
u10,1
u9,1
u8,1
u7,1
u10,2
u9,2
u8,2
u7,2
u10,3
u9,3
u8,3
u7,3
u10,4
u9,4
u8,4
u7,4
20°C
100°C

## Slide 13: Restrictions
There is one restriction to this algorithm:
  A reasonable strategy: given a and h, suppose we want to approximate the solution from t0 to tf
    We want so
    Thus, let’s ensure
    That is,

## Slide 14: Implementation
function [xs, ts, Us] = heat( alpha, x_rng, t_rng, u_init, u_bndry, nx )
h = (x_rng(2) - x_rng(1))/nx;
nt = ceil( 4.0*alpha*(t_rng(2) - t_rng(1))/h^2 )
dt = (t_rng(2) - t_rng(1))/nt
xs = linspace( x_rng(1), x_rng(2), nx + 1 )';
ts = linspace( t_rng(1), t_rng(2), nt + 1 );
Us = zeros( nx + 1, nt + 1 );
for k = 2:nx
Us(k, 1) = u_init( xs(k) );
end
Us([1, nx+1], 1) = u_bndry( ts(1) );
for ell = 1:nt
for k = 2:nx
Us(k, ell + 1) = Us(k, ell) ...
+ alpha*dt*(Us(k-1, ell) - 2*Us(k, ell) + Us(k+1, ell))/h^2;
end
Us([1, nx+1], ell+1) = u_bndry( ts(ell+1) );
end
end
alpha
The diffusivity coefficient
x_rng
A 2-dimensional vector [a, b]
t_rng
A 2-dimensional vector [t0, tf]
u_init
A function of the spatial variable x that gives the initial state at that point
u_bndry
A function of the time variable t that returns a 2-dimensional vector giving the left and right boundary values at that point in time
nx
The number of sub-intervals we will break the interval [a, b] into

## Slide 15: Implementation
Why not just program this in C++?
  It seems like a straight-forward translation
Matlab is an interpreted language, meaning it is, in general, slow
  There are, however, functions, that simply call compiled routines
  Calling a compiled routine can be as fast as authoring that function in C++
Where can we accomplish such a speed up?

## Slide 16: Implementation
Many vector-based functions execute faster than a corresponding for loop:
    for k = 2:nx
    Us(k, 1) = u_init( xs(k) );
    end
    Us(2:nx, 1) = u_init( xs(2:nx) );
  This requires that u_init work on a vector-valued argument
    u1_init = @(x)( 20.0 );
    u1_init = @(x)( 20.0*ones( size( x ) );

## Slide 17: Implementation
Additionally, the operation of calculating xk+1 – 2xk + xk–1 is so common, there is a Matlab function to repeated perform this:
    diff( x ); # This has one fewer entries
    x(2) - x(1)
    x(3) - x(2)
    .
    .
    .
    x(end) - x(end-1)
    diff( x, 2 ); # This has two fewer entries
    x(3) - 2*x(2) + x(1)
    x(4) - 2*x(3) + x(2)
    .
    .
    .
    x(end) - 2*x(end-1) + x(end-2)

## Slide 18: Implementation
function [xs, ts, Us] = heat( alpha, x_rng, t_rng, u_init, u_bndry, nx )
h = (x_rng(2) - x_rng(1))/nx;
nt = ceil( 4.0*alpha*(t_rng(2) - t_rng(1))/h^2 )
dt = (t_rng(2) - t_rng(1))/nt
xs = linspace( x_rng(1), x_rng(2), nx + 1 )';
ts = linspace( t_rng(1), t_rng(2), nt + 1 );
Us = zeros( nx + 1, nt + 1 );
Us(2:nx, 1) = u_init( xs(2:nx) );
Us([1, nx+1], 1) = u_bndry( ts(1) );
for ell = 1:nt
Us(2:nx, ell + 1) = Us(2:nx, ell) + alpha*dt*diff( Us(:, ell), 2 )/h^2;
Us([1, nx+1], ell+1) = u_bndry( ts(ell+1) );
end
end

## Slide 19: Example 1
Consider this example:
>> u1_init = @(x)( 20.0*ones( size( x ) ) );
>> u1_bndry = @(t)( [0.0, 100.0]' );
>> [x1s, t1s, U1s] = heat( 0.3, [0, 1], [0, 0.5], u1_init, u1_bndry, 10 );
>> mesh( t1s, x1s, U1s );

## Slide 20: Example 1
Recalling that nx = 10, we see how the temperature changes over time

## Slide 21: Example 2
Consider this example:
>> u1_init = @(x)( 20.0*ones( size( x ) ) );
>> u2_bndry = @(t)( (t > 0.25)*[0.0, 80.0]' + [0.0, 20.0]' );
>> [x2s, t2s, U2s] = heat( 0.3, [0, 1], [0, 0.5], u2_init, u2_bndry, 10 );
>> mesh( t2s, x2s, U2s );

## Slide 22: Example 2
It starts to cool on the one side, but then the other side starts to heat up after 0.25 seconds

## Slide 23: Error analysis
Recall the formula using h was O(h2), but the formula using Dt was O(Dt)
  Recall, however, that
  Thus, so if the error is O(Dt), it is also O(h2)

## Slide 24: Neumann boundary conditions
What happens if one boundary is insulated or has a Neumann boundary condition?
  Recall, in our code, we
    Calculated the next interior points
    Then set the boundary conditions for that same ℓ
ℓ
k
uk,ℓ
0
1
2
3
4
5
6
7
8
9
10
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14

## Slide 25: Neumann boundary conditions
Recall from the last topic, we saw that if a boundary satisfied a Neumann condition, the following were true:
Suppose a boundary has a Neumann condition:
  Calculated the next interior points
  Calculate the boundary value based on the Neumann condition

## Slide 26: Implementation
function [xs, ts, Us] = heat( alpha, x_rng, t_rng, u_init, u_bndry, u_dirichlet, nx )
h = (x_rng(2) - x_rng(1))/nx;
nt = ceil( 4.0*alpha*(t_rng(2) - t_rng(1))/h^2 )
dt = (t_rng(2) - t_rng(1))/nt
xs = linspace( x_rng(1), x_rng(2), nx + 1 )';
ts = linspace( t_rng(1), t_rng(2), nt + 1 );
Us = zeros( nx + 1, nt + 1 );
Us(2:nx, 1) = u_init( xs(2:nx) );
Us([1, nx+1], 1) = u_bndry( ts(1) );
for ell = 1:nt
Us(2:nx, ell + 1) = Us(2:nx, ell) + alpha*dt*diff( Us(:, ell), 2 )/h^2;
Us([1, nx+1], ell+1) = u_bndry( ts(ell+1) );
end
end

## Slide 27: Implementation
function [xs, ts, Us] = heat( alpha, x_rng, t_rng, u_init, u_bndry, u_dirichlet, nx )
# Initialization...
dirichlet = u_dirichlet( ts(1) );
boundary = u_bndry( ts(1) );
if dirichlet(1)
Us(1, 1) = boundary(1);
else
Us(1, 1) = -2.0/3.0*boundary(1)*h + 4.0/3.0*Us(2, 1) - 1.0/3.0*Us(3, 1);
end
if dirichlet(2)
Us(nx+1, 1) = boundary(2);
else
Us(nx+1, 1) = 2.0/3.0*boundary(2)*h + 4.0/3.0*Us(nx, 1) - 1.0/3.0*Us(nx-1, 1);
end
# Populate the balance of the matrix 'Us'
end

## Slide 28: Implementation
for ell = 1:nt
Us(2:nx, ell + 1) = Us(2:nx, ell) + alpha*dt*diff( Us(:, ell), 2 )/h^2;
dirichlet = u_dirichlet( ts(ell + 1) );
boundary = u_bndry( ts(ell + 1) );
if dirichlet(1)
Us(1, ell+1) = boundary(1);
else
Us(1, ell+1) = -2.0/3.0*boundary(1)*h + 4.0/3.0*Us(2, ell+1) ...
- 1.0/3.0*Us(3, ell+1);
end
if dirichlet(2)
Us(nx+1, ell+1) = boundary(2);
else
Us(nx+1, ell+1) = 2.0/3.0*boundary(2)*h + 4.0/3.0*Us(nx, ell+1) ...
- 1.0/3.0*Us(nx-1, ell+1);
end
end
end

## Slide 29: Example 3
Consider this example:
>> u3_in = @(x)(x.^2);
>> u3_by = @(t)( [0.0, 0.0]' );
>> u3_dt = @(5)( [false, false]' );
>> [x3s, t3s, U3s] = heat( 0.3, [0, 1], [0, 0.5], u3_in, u3_by, u3_dt, 10 );
>> mesh( t3s, x3s, U3s );

## Slide 30: Example 3
The temperature will approach the average temperature

## Slide 31: Example 4
Consider this example:
>> u4_in = @(x)( 20.0*ones( size( x ) ) );
>> u4_by = @(t)( [0.0, 100.0]' );
>> u4_dt = @(5)( [false, true]' );
>> [x4s, t4s, U4s] = heat( 0.3, [0, 1], [0, 0.5], u4_in, u4_by, u4_dt, 10 );
>> mesh( t4s, x4s, U4s );

## Slide 32: Example 4
Note the temperature heats up across the length
  It will approach a uniform temperature of 100°C

## Slide 33: Summary
Following this topic, you now
  Understand how to approximate the heat equation with a finite-difference equation
  Have seen how to approximate the solution to the heat equation given both initial states and boundary values in one dimension
  Are aware of how to implement such a solution in Matlab
  Have seen two examples
  Understand how to deal with insulated boundary conditions with implementations and examples

## Slide 34: References
[1] https://en.wikipedia.org/wiki/Heat_equation

## Slide 35: Acknowledgments
None so far.

## Slide 36: Colophon
These slides were prepared using the Cambria typeface. Mathematical equations use Times New Roman, and source code is presented using Consolas. Mathematical equations are prepared in MathType by Design Science, Inc.
Examples may be formulated and checked using Maple by Maplesoft, Inc.
The photographs of flowers and a monarch butter appearing on the title slide and accenting the top of each other slide were taken at the Royal Botanical Gardens in October of 2017 by Douglas Wilhelm Harder. Please see
https://www.rbg.ca/
for more information.

## Slide 37: Disclaimer
These slides are provided for the ece 204 Numerical methods course taught at the University of Waterloo. The material in it reflects the author’s best judgment in light of the information available to them at the time of preparation. Any reliance on these course slides by any party for any other purpose are the responsibility of such parties. The authors accept no responsibility for damages, if any, suffered by any party as a result of decisions made or actions based on these course slides for any other purpose than that for which it was intended.